## Slide 1: Cli Tool User Guide
2018.01.19

## Slide 2: Cli install setup in Amlogic Platform
檢查 wifi interface 是否正常
  需確認開機前先全完斷電，否則可能造成下次USB interface無法重新認卡，可能會造成wifi interface無法帶起
第一次使用adb 時，需讓amlogic platform去信任NB/PC主機(透過GUI)
如果利用USB port來進行adb command，USB port type 需為 OTG
-請參閱Pag 3 & Page4
Non-adb 時的cli install setup
-請參閱Pag 5
在進行RF tool前，需確認無wireless連線,並確認硬體架構設定
-請參閱Pag 6 & Page 7

## Slide 3: adb install & adb command
Install adb command (如果電腦上沒有adb-tool就必須安裝)
  http://bernaerts.dyndns.org/linux/74-ubuntu/328-ubuntu-trusty-android-adb-fastboot-qtadb
  備註:adbUbuntu 14.04 - Install Android Tools
Amlogic platform adb command
  adb root
  adb remount
  adb shell

## Slide 4: rf & cli install (adb)
Push rf and cli to device(Amlogic)
  adb push rf /system/bin/rf
  adb push cli /system/bin/cli(更改執行權)
Change rf and cli mode
  adb shell
  chmod 777 /system/bin/rf
  chmod 777 /system/bin/cli

## Slide 5: rf & cli install (non-adb)
Console command
  mkdir /data/temp
  mount –o rw,remount /system
    [change filesystem /system to read/write]
  mount –t vfat /dev/block/sda1 /data/temp
    [mount usb storage to /data/temp]
  cp /data/temp/rf /system/bin/rf
  cp /data/temp/cli /system/bin/cli
  chmod 777 /system/bin/rf
  chmod 777 /system/bin/cli
  umount /data/temp

## Slide 6: Hardware Setup
SSV6266P
GND/RX/TX
UART
amlogic platform S905
HDMI
  25MHz晶振
OTG Port
Ant端

## Slide 7: Hardware Setup
在進行RF tool前，需確認無wireless連線
如果利用USB port來進行adb command，USB port type 需為 OTG
amlogic platform S905
Non-adb時須利用UART來操作

## Slide 8: rf command
rf [tx|rx|stop|rate|count|reset|ifs|freq|rfreq|rssi|sar|ch]
  tx command
    Set rf block mode
    Disable ack policy
    Set channel 1 bandwidth 20, rate HT20, MCS7
    Tx packet generate (default ifs 15us)
  rx command
    Set rf block mode
    Set channel 1, bandwith20
    Disable ack policy
    Mib reset

## Slide 9: rf command
rf [tx|rx|stop|rate|count|reset|ifs|freq|rfreq|rssi|sar|ch]
  stop
    Rf unblock mode
  rate [rate index]
    Set rate index
  count [0|1]
    Get phy mib, 0 => 11b mib, 1 => 11gn mib
  reset
    Mib reset
  ifs [value]
    Set txgen packet ifs value

## Slide 10: rf command
  rf [tx|rx|stop|rate|count|reset|ifs|freq|rfreq|rssi|temperature|ch]
  freq [value]
    Set xtal frequency offset
  rfreq
    Get xtal frequency offset
  rssi
    get ofdm/b mode rssi of last packet
  temperature
    Ic temperature
  ch [channel value] [bw40]
    Set channel

## Slide 11: Change channel command
rf ch [ch_value] [bw40]
  Manual command to change channel
  Ex:rf_tool ch 3: change channel to 3 ht20.
  rf_tool ch 3 bw40: change channel to 3 bandwith 40
  chan3 bw 40 = chan 1 HT40PLUS
  = chan 5 HT40MINUS

## Slide 12: TX_Cli_command
TX test Cli_command
rf tx
rf rate 22
rf ch 1

## Slide 13: RX_Cli_command
RX test Cli_command
rf rx
rf ch 1
rf reset
rf count [1|0]
]

## Slide 14: Set RF tool tx rate
rf rate [rateidx]
rateidx | description | rateidx | description | rateidx | description | rateidx | description
0 | 11b, 1M | 7 | 11g, 6M | 14 | 11g, 54M | 21 | Ht20, MCS6, LGI
1 | 11b, 2M | 8 | 11g, 9M | 15 | Ht20, MCS0, LGI | 22 | Ht20, MCS7, LGI
2 | 11b, 5.5M | 9 | 11g, 12M | 16 | Ht20, MCS1, LGI | 23 | Ht20, MCS0, SGI
3 | 11b, 11M | 10 | 11g, 18M | 17 | Ht20, MCS2, LGI | 24 | Ht20, MCS1, SGI
4 | None | 11 | 11g, 24M | 18 | Ht20, MCS3, LGI | 25 | Ht20, MCS2, SGI
5 | 11b, 5.5M Short Preamble | 12 | 11g, 36M | 19 | Ht20, MCS4, LGI | 26 | Ht20, MCS3, SGI
6 | 11b, 11M Short Preamble | 13 | 11g, 48M | 20 | Ht20, MCS5, LGI | 27 | Ht20, MCS4, SGI

## Slide 15: Set RF tool tx rate
rf rate [rateidx]
rateidx | description | rateidx | description | rateidx | description
28 | Ht20, MCS5, SGI | 35 | Ht40, MCS4, LGI | 42 | Ht40, MCS3, SGI
29 | Ht20, MCS6, SGI | 36 | Ht40, MCS5, LGI | 43 | Ht40, MCS4, SGI
30 | Ht20, MCS7, SGI | 37 | Ht40, MCS6, LGI | 44 | Ht40, MCS5, SGI
31 | Ht40, MCS0, LGI | 38 | Ht40, MCS7, LGI | 45 | Ht40, MCS6, SGI
32 | Ht40, MCS1, LGI | 39 | Ht40, MCS0, LGI | 46 | Ht40, MCS7, SGI
33 | Ht40, MCS2, LGI | 40 | Ht40, MCS1, SGI |  | 
34 | Ht40, MCS3, LGI | 41 | Ht40, MCS2, SGI |  | 

## Slide 16: CLI CALIBRATION
cli cali do|show|dpd
  cli cali do: re-do calibration.
  cli cali show: show current calibration result.
  cli cali dpd do|show|enable|disable
    cli cali dpd do: re-do padpd for current channel
    cli cali dpd show: show dpd result for all band.
    cli cali dpd enable: enable dpd
    cli cali dpd disable: disable dpd.